# Environmentally Preferable landscaping service 
Small Purchase Attachment

# Instructions: 
Small purchase solicitations/request for quotations for landscaping services shall either incorporate environmental contract language and requirements into the requirements section of the statement of work or include them as an attachment. The following document is designed to serve as the environmental requirements small purchase attachment for landscaping services. Prior to using, please review to ensure all requirements listed are relevant to your solicitation. For guidance on utilizing the language below, please see the Statement of Work Guidance Document which contains guidance on utilizing each section of contract language and how to modify the language to reflect the specific needs of your procurement. Supporting solicitation documents and resources can be accessed here.

Landscaping services shall comply with the environmental requirements noted below.

# Background

The District of Columbia is committed to procuring quality goods and services in a timely manner and reasonable cost that support the District meeting its sustainability goals. The District aims to improve worker health, conserve natural resources, and prevent pollution through this activity. Environmental components to be considered include: recycled content and recyclability; energy efficiency; and the presence of undesirable materials in the products, especially toxic chemicals which are persistent and bio-accumulative. Environmental requirements related to sustainability and environmentally preferable purchasing goals are embedded throughout this contract.

Definitions

These terms when used in this solicitation have the following meanings:

Bioretention are practices that capture and store stormwater runoff and pass it through a filter bed of engineered soil media of sand, soil, and organic matter to remove contaminants and sediments.  .

Compost refers to a stable, organic substance produced by a controlled decomposition process that can be used as a soil additive, fertilizer, growth media, or other beneficial use (Applicable Document #18).

Composting refers to the series of activities, including separation, collection, and processing, through which materials are recovered or otherwise diverted from the solid waste steam for conversion into compost (Applicable Document #18).

Cultivar refers to a plant variety that has been produced in cultivation by selective breeding. Cultivars can be noted by the presence of a name in quotations appended to the scientiﬁc name. For example, a cultivar of Black-eyed Susan is Rudbeckia fulgida ‘Goldstrum’.

Enhanced efficiency fertilizer refers to a fertilizer product with characteristics that allow increased plant uptake and reduces the potential of nutrient loss to the environment, such as gaseous loss, leaching, or runoff, when compared to an appropriate reference fertilizer product.

Environmentally Preferable Product or Service (EPPS) refers to a good or service that is less harmful to human health and the environment when compared with competing goods or services that serve the same purpose. The factors to be compared include raw materials acquisition, production, manufacturing, packaging, distribution, reuse, operation, maintenance, or disposal of the product. Information on EPPSs recognized by the District and their corresponding EPPS requirements can be found here: http://ocp.dc.gov/page/district-columbia-sustainable-specifications.

Fertilizer refers to a material that contains one or more nutrients intended to promote plant growth.

Habitat Restoration Areas are areas designated and managed by the District Department of Environment’s (DDOE) Habitat Restoration Program where restoration activities are planned or are being undertaken to protect and restore river, stream and wetland habitats in the District of Columbia with the intent of improving water quality in the District’s waterways and improve the ecological diversity found within the District’s borders. All relevant Habitat Restoration Areas included in the contract will be noted as such.

Integrated Pest Management is a method of managing pests that minimizes harm to the environment by using comprehensive information on the life cycle of pests and their interaction with the environment.

Invasive plants are non-native plants that cause economic, environmental harm, or harm to human health. For purposes of this specification, invasive plants are defined as any species that appears in the U.S. Fish and Wildlife Service’s “Plant Invaders of Mid-Atlantic Natural Areas,” and/or any other species that the District deems “invasive.”

Locally grown plants are any plants sourced from nurseries in DC, PA, OH, MD, VA, WV, DE, or NJ.

Locally sourced seeds or plant material refers to the origins of the seeds or plant material for a grown plant being purchased. The location of the source of seeds or plant material may differ from the location of the grown plant that is procured. For this specification, locally sourced seeds or plant material is defined as any plant material grown from plant or seeds sourced from DC, PA,, OH, MD, VA, WV, DE, or NJ.

Low impact development seeks to minimize stormwater runoff from a given site. Low impact development projects include green roofs, bioretention/rain gardens, rain barrels, downspout disconnections, permeable pavement, native plant landscaping and a host of other innovative ideas that combine to stop pollution from reaching our rivers and streams.

Native plants are plant species that occurs naturally in a particular region, state, ecosystem, and habitat without direct or indirect human actions. In the mid-Atlantic region, this includes plant species that existed prior to European contact, or any plant species that have since been established in the region through natural processes uninfluenced by human activity. For purposes of this specification, native plants are defined as any species that appears in the U.S. Fish and Wildlife Service’s Native Plants for Wildlife Habitat and Conservation Landscaping Chesapeake Bay Watershed, Prince George’s County Bioretention Manual, or is indicated as being native in the District Department of Transportation Green Infrastructure Standards

Natural Areas refers to District of Columbia- owned wetlands, woodlands, and meadows.

Material Safety Data Sheet (MSDS) refers to a document that contains information on the potential hazards of a chemical product and how to work safely with the product. The MSDS also contains information on the use, storage, and handling of the hazardous material, and how to respond in case of an accident or spill. The MSDS contains much more information about the material than the product label. However, it is important to note that the MSDS may not list every human and environmental impact associated with the product.

Ornamental landscaping is landscaping that includes turf and commercially available horticultural plants introduced to a particular location to contribute to the aesthetics of the area and/or to provide shade.

Recycling is the series of activities, including separation, collection, and processing, through which materials are recovered or otherwise diverted from the solid waste stream for use as raw materials or in the manufacture of products other than fuel.

Soil test refers to a scientific measurement that determines the nutrient level of a soil.

Stormwater or stormwater runoff is rainfall that does not soak into the ground, but instead flows over the land’s surface into the nearest water body through storm drain channels. The District seeks to reduce stormwater runoff because it collects and carries along pollution wherever it flows.

Waterbody refers to a wetland, watercourse, river, stream, creek, stormwater retetention or detention basin, or other similar water resource.

Turf refers to areas that are covered in grass and are used for athletic purposes or general green space used in recreational activities.

Environmental Requirements

Plant Material

- All plant species shall be approved by the District prior to purchase and installation.

- The contractor shall comply with the following native plant and cultivar requirements when procuring or installing new plant material in fulfillment of the contract.

  - A minimum of 80% of plants purchased by the Contractor for installation in planted or landscaped beds shall be native plants. For the purposes of this requirement, “native plants” refers to plants listed in the U.S. Fish & Wildlife Service’s Native Plants for Wildlife Habitat and Conservation Landscaping Chesapeake Bay Watershed. Native plant cultivars may be utilized in fulfillment of this requirement.

  - 100% of plants purchased by the Contractor for installation in natural areas or habitat restoration areas shall be native plants. For the purposes of this requirement, “native plants” refers to plants listed in the U.S. Fish & Wildlife Service’s Native Plants for Wildlife Habitat and Conservation Landscaping Chesapeake Bay Watershed. Native plant cultivars shall not be utilized in fulfillment of this requirement.

  - 100% of plants purchased by the Contractor for installation in bioretention or low impact development sites shall be native plants. For the purposes of this requirement, native plants refer to plants listed in either Prince George’s County Bioretention Manual or indicated as being native in the District Department of Transportation’s Green Infrastructure Standards. Native plant cultivars shall not be utilized in fulfillment of this requirement.

  - The purchase of native plants shall be prioritized by the Contractor for installation for street trees (right of way planting). For the purposes of this requirement, native plants include plants indicated as being native in the District Department of Transportation Green Infrastructure Standards. Cultivars may be utilized in fulfillment of this requirement.

- The contractor shall comply with the following locally grown plant requirements when procuring or installing new plant material in fulfillment of the contract.

  - For the purposes of this contract, local is defined as DC, PA, OH, MD, VA, WV, DE, or NJ.

  - Annuals, perennials, shrubs, and trees purchased for installation on District property shall be grown from locally sourced seeds or plant material.

  - Annuals, perennials, and shrubs purchased for installation on District property shall be locally grown.

  - Trees purchased for installation on District property shall be grown locally wherever practical.

- The Contractor shall not purchase or install invasive plants on District property. For the purposes of this requirement, invasive plants refers to plants listed in the U.S. Fish & Wildlife Service’s Plant Invaders of Mid-Atlantic Natural Areas or on other lists of invasive plants provided by the designated District point of contact during the course of the contract.

Fertilizing

- Contractors shall fully comply with the requirements below which are based upon requirements set forth in Section 203 of the Anacostia River Clean Up and Protection Fertilizer Act of 2012.

- Applying Fertilizer to Turf

  - Fertilizer may be applied only to turf:

    - Beyond a 15-foot buffer area from a water body; provided, that fertilizer may be applied beyond a 10-foot buffer area if a drop spreader, rotary spreader with a deflector, or targeted spray liquid is used for the fertilizer application;

    - When sufficient water is applied to the soil within 24 hours of application to immobilize the fertilizer and prevent fertilizer loss by runoff or when soil is sufficiently saturated to immobilize the fertilizer and prevent fertilizer loss by runoff;

    - When a heavy rainfall is not occurring or not predicted to occur, and when soils are not saturated and the potential for fertilizer movement off-site exists;

    - After March 1st and before November 15th in a calendar year;

    - When the ground is not frozen; and

    - In an amount consistent with an annual recommended rate established by the District Department of the Environment and detailed below.

  - Applying Fertilizer Containing Nitrogen to Turf

    - A fertilizer containing nitrogen may be applied to turf only if the fertilizer is at least 20% slow release.

    - A fertilizer containing nitrogen may be applied to turf only at an application rate of less than 0.7 pounds per 1,000 feet of water-soluble nitrogen, and at an application rate of less than 0.9 pounds per 1,000 square feet of total nitrogen.

    - Notwithstanding the preceding requirement, an enhanced efficiency fertilizer containing nitrogen that has a release rate of less than 0.7 pounds per 1,000 square feet of total nitrogen per month may be applied at an annual application rate of less than 2.5 pounds per 1,000 square feet of nitrogen. The annual total application rate may not exceed 80% of the annual recommended rate for total nitrogen, as established by the District Department of Environment.

  - Applying Fertilizer Containing Phosphorous to Turf

    - A low phosphorus fertilizer may be applied to turf if a soil test conducted within the previous 3 years indicates that the level of phosphorus in the soil is insufficient to establish, reestablish, repair, or support adequate turf growth.

      - A low phosphorus fertilizer refers to a fertilizer containing no more than 5% of available phosphate (P2O5), and that has an application rate not to exceed 0.25 pound of available phosphate (P2O5)/1,000 square feet/application and 0.5 pound of available phosphate (P2O5)/1,000 square feet/year.

    - A fertilizer that contains phosphorus in an amount greater than 0.67% phosphate by weight may be applied to turf if the soil test indicates that the level of phosphorus in the soil is insufficient to establish or reestablish turf. The application of fertilizer allowed under this paragraph shall not exceed the amount or rate of application of fertilizer recommended by the soil test, as determined by the District Department of the Environment.

  - Fertilizer may not be applied to an impervious surface or be stored in a container on an impervious surface in a manner that would permit fertilizer runoff. Fertilizer that is inadvertently applied or leaked onto an impervious surface shall be returned for reuse to the target surface or to either its original or another appropriate container.

Debris Removal

- The Contractor shall dispose of grass clippings, plant waste, and other forms of landscaping debris as appropriate, through composting or other forms of recycling rather than delivery to a landfill. This provision shall only be required if the District is able to provide the contractor with a suitable location for the delivery of plant waste for composting or recycling. The Contractor shall dispose of all debris in accordance with local, state, and federal regulations.

Integrated Pest Management

- Consistent with the Pesticide Education and Control Amendment Act of 2012 and Pesticide Operation Regulations, all pesticide management and/or application shall be conducted in accordance with the contracting agency’s Integrated Pest Management (IPM) policy.

- Consistent with the Pesticide Education and Control Amendment Act of 2012 and Pesticide Operation Regulations, no person shall apply any pesticide to public rights-of-way, parks, District-occupied buildings, other District property, or child-occupied facilities if the location does not have an IPM program approved by the District Department of the Environment.

- The Contractor shall ensure that all staff applying pesticides in buildings or on grounds shall be licensed to apply pesticides and trained and knowledgeable in the principles and practices of IPM.

- The Contractor shall provide copies of the company pest control license and dated pesticide applicator certificates for every employee who will be performing on-site services under this contract.

- The pesticides used by the Contractor shall be registered with the United States Environmental Protection Agency (E.P.A.) and the District of Columbia.

- The Contractor and staff shall follow Pesticide Operation Regulations and label precautions and shall comply with the IPM Program when utilizing pesticides in fulfillment of this contract.

- The Contractor shall develop an IPM Plan that aligns with the requirements outlined in the contract and the District’s IPM policy that addresses the following:

  - Structural or Operational Changes: The Contractor shall describe site specific solutions for eliminating pest access, food, water, and harborage.

  - Monitoring: The Contractor shall describe the products and procedures used for identification of pest presence, access and harborage locations.

  - Materials and Equipment: The Contractor shall provide labels and Material Safety Data Sheets (MSDS) for all pesticide products to be used.  In addition, brand names shall be provided for all application equipment, rodent bait boxes, monitoring and trapping devices, and any other control equipment that may be used to provide service.

  - Service Schedule:  The Contractor shall provide service schedules that include the frequency of Contractor visits.

- The Contractor’s staff shall develop an IPM Service Report to be submitted to the Building Manager and Contract Administrator at the frequency specified in the agency’s Integrated Pest Management policy. The IPM Service Report shall contain a record of inspections and what was checked, what was found, and what nonchemical and chemical control actions implemented by the IPM Technician, description of any pesticides applied, a detailed description of the treatment, the site, the application rate, and the amount applied.

Engine Idling

- In fulfillment of the requirements of this solicitation, the Contractor shall not allow the engine of a motor vehicle to idle for more than three minutes while the motor vehicle is parked, stopped, or standing except:

  - To operate private passenger vehicles;

  - To operate power takeoff equipment, including dumping, cement mixers, refrigeration systems, content delivery, winches, or shredders; or

  - To idle the engine for no more than five (5) minutes to operate heating equipment when the ambient air temperature is thirty-two degrees Fahrenheit (32° F) or below.

Landscaping Personnel and Administrative Requirements

- All employees performing ornamental landscaping shall have one or more or the following certifications or have a certification or experience deemed to be equivalent by the designated District point of contact: State of Maryland Certified Professional Horticulturist, State of Virginia Certified Horticulturalist, or Landscape Contractors Association MD, DC, VA Certified Landscape Technician.

- All employees performing tree and shrub pruning shall be an ISA Certified Arborist or have certification or experience deemed to be equivalent by the designated District point of contact.

Reporting

The Contractor shall document that the products and services supplied under this contract comply with key environmental criteria noted above.  The Contractor shall submit the following information to the designated District point of contact, as noted in the Section F Deliverables.

- Plant Material Report – To be provided annually or as requested in Excel and delivered via email. The report shall include:

  - Date of purchase

  - Name of company from which plant species were sourced

  - Plant species purchased

  - Quantity purchased

  - State from which plant was sourced

  - State of origin for seeds or plant material from which plant was grown

  - Indicate whether the plant species is in compliance with the solicitation’s native plant requirement

  - Indicate whether the plant species purchased is in compliance with the solicitation’s invasive plant requirement

  - Price per unit

  - Total spend on purchased plants

- Integrated Pest Management Plan - To be provided within 30 days of signing the contract, and annually thereafter or whenever changes have been made. The plan shall be provided in Word, Excel or PDF and delivered via email. The plan shall address the Integrated Pest Management Plan requirements outlined in Section C.5.

- Integrated Pest Management Service Report - To be provided at the frequency specified in the agency’s Integrated Pest Management Plan and submitted to the specified District point of contact. The plan shall be provided in Word, or Excel and delivered via email. The plan shall address the Integrated Pest Management Plan requirements outlined in Section C.5.

- Integrated Pest Management and Pesticide Licensing and Training Documentation - To be provided upon contract signing and annually thereafter in Word, Excel, or PDF and delivered via email. The report shall include:

  - Company pesticide application license

  - A listing of all pesticide applicators providing pesticide services in fulfilment of the contract, and a copy of each applicator’s up-to-date license

  - IPM training records for employees

- Annual Fertilizer Application Report – To be provided on March 1 of each calendar year in Excel and delivered via email to the contract administrator, and the designated contact at the District Department of Environment’s Watershed Protection Division. The report shall include:

  - Contractor name

  - Contract award number

  - PO no.

  - Acres fertilized

  - Amount of fertilizer applied (in pounds)

  - Percent of nitrogen and phosphorous by weight in fertilizer applied

  - Application rate of applied fertilizer

- Landscaping Personnel and Administrative Requirements Report – To be provided upon contract signing and on an annual basis in Word, PDF, or Excel via email. The Report shall include:

  - Names of personnel performing ornamental landscaping and pruning services

  - Certifications received

  - Certification expiration date